CSCI 264: Assembly Language Subprograms and Stack

Example:

| Command | Object address | Hex code |
| --- | --- | --- |
| MOV ESP, 01234H | 0 | BC 34 12 00 00 |
| IN EAX, [0] | 5 | E5 00 |
| MOV EBX, EAX | 7 | 89 C3 |
| CALL sign | 9 | E8 …… |
| OUT [1], EAX | E | E7 01 |
| RET | 10 | C3 |
| sign: | 11 |  |
| MOV ECX, 0 | 11 | B9 00 00 00 00 |
| CMP EBX, 0 | 16 | 81 FB 00 00 00 00 |
| JE ZER | 1C | 0F 84 10 00 00 00 |
| JG POS | 22 | 0F 8F 14 00 00 00 |
| MOV EAX, 2 | 28 | B8 02 00 00 00 |
| JMP END | 2D | E9 0F 00 00 00 |
| ZER: MOV EAX, 0 | 32 | B8 00 00 00 00 |
| JMP END | 37 | E9 05 00 00 00 |
| POS: MOV EAX, 1 | 3C | B8 01 00 00 00 |
| END: RET | 41 | C3 |

Stack:

| Memory address | Value |
| --- | --- |

ESP:

Assembly and High Level Languages ( C / C++)

Parameter Passing

Example:

C code:

#include <ctype.h>

int main(){

int x, y;

x = 65;

y = tolower ( x );

return 0;

}

Assembler code of this program:

MOV EBX, 65

PUSH EBX

CALL tolower

ADD ESP, 4

Returned integer values are stored in EAX, in C/C++ calling program is popping the parameters.

C/ C++ pushes parameters starting from the right:

Example:

int ipow ( int base, int exponent);

assembler code to call this function to calculate 2^3 is:

MOV EBX, 3

PUSH EBX

MOV EBX, 2

PUSH EBX

CAL ipow

ADD ESP, 8

After this call, the result ipow ( 2, 3) = 8 will be stored in EAX

Calling Assembler from C

Example: (Program 7.7 and 7.8 from your textbook)

;half subprogram

global half          ; in Edlinas  .globl half

half:    PUSH ECX

MOV ECX, [ESP+8]

MOV EAX, 0

AGN: INC EAX

SUB ECX, 2

JG AGN

JZ DUN

MOV EAX, 0

DUN: POP ECX

RET

This code will be stored in file half.asm

This code can be compiled using NASM assembler as follows:

nasm –f elf half.asm

The object file will be produced:  half.o

Important: 1. add global name to the assembly code

2. push the register that will be used for computations

3. store the return value in EAX

C++ code: ( stored in file collatz.c)

#include <iostream>

using namespace std;

extern “C” int half ( int y);

int main (){

int count =0, x, y;

cout << “Please enter the number\n”;

cin >> x;

while ( x !=0){

count++;

y = half ( x );

if ( y!=0)

x = y;

else

x = x*3+1;

}

cout << “the number of steps is “ << count << endl;

return 0;

}

To compile and link half.o type the following at Linux prompt:

g++ collatz.c half.o

Recursion

Example:  recursive function that calculates 1+2+3 +.. +n:

Recursive definition:

sum(n)= 0, if n=0

sum(n)=sum(n-1)+n, if n>0

Assembly code:

global sum

sum:    push ecx

move eax, [esp+8]

cmp eax, 0

ja els

move eax, 0

jmp dun

els:       mov ecx, eax

dec eax

push eax

call sum

add esp, 4

add eax, ecx

dun:      pop ecx

ret

The C++ code that will call to this function

#include <iostream>

using namespace std;

extern “C” int sum ( int n );

int main(){

cout << “please enter the non-negative integer \n”;

int n, y;

cin >> n;

y = sum ( n );

cout << y;

return 0;

}

Run-time stack for the different values of n:

I will denote the address of the statement after function call by FF FF FF FF – it’s not a real address.

I will denote the garbage value by ** ** ** **

n=0

| address | value | explanation |
| --- | --- | --- |
| ESP after push ECX inside the function | ** | push ecx – the value that |
|  | ** | was in ecx will be pushed |
|  | ** | into the stack |
|  | ** |  |
| ESP after push return address | FF | address of the next |
|  | FF | statement after |
|  | FF | function call |
|  | FF | pushed into Stack |
| ESP after push parameter | 00 | parameter n=0 |
|  | 00 | pushed inside the |
|  | 00 | stack |
|  | 00 |  |
| ESP initial |  |  |

mov eax, [esp+8] – eax will get the value of parameter ( 0 in our example)

cmp eax, 0

ja els ; in this example no jump , eax = 0

mov eax, 0 ; mov the final result into eax

jmp dun

…

…

…

dun:     pop ecx    ; the esp will come back to the return address, ecx will get the garbage

; value but it doesn’t affect anything

ret ; the esp will come back to the address of the parameter

after the program will return to main the following command will be performed in the “background”:

add esp, 4 – it will return the value of the stack to the initial position

n = 1

| address | value | explanation |
| --- | --- | --- |
| esp after push ecx | 01 |  |
|  | 00 |  |
|  | 00 |  |
|  | 00 |  |
| esp after call sum that pushes the return | FF |  |
| address into the stack | FF |  |
| In this case this is the address of | FF |  |
| command add esp, 4 | FF |  |
| ESP after PUSH EAX | 00 | the new value of parameter |
|  | 00 | pushed into the Stack |
|  | 00 |  |
|  | 00 |  |
| ESP after push ECX inside the function | ** | push ecx – the value that |
|  | ** | was in ecx will be pushed |
|  | ** | into the stack |
|  | ** |  |
| ESP after push return address | FF | address of the next |
|  | FF | statement after |
|  | FF | function call |
|  | FF | pushed into Stack |
| ESP after push parameter | 01 | parameter n=0 |
|  | 00 | pushed inside the |
|  | 00 | stack |
|  | 00 |  |
| ESP initial |  |  |

Execution of the program for n =1:

mov eax, [esp+8]         ;eax will get the value of parameter ( 1 in our example)

cmp eax, 0

ja els                            ; in this example we will jump, eax = 1

…

els:      mov ecx, eax           ; ecx will get 1

dec eax                    ; eax gets 0 ( the parameter for the recursive call)

push eax                  ; n-1 ( now is 0 ) – new parameter - pushed into the stack

call sum                  ; into the stack the value of the return address will be pushed

; the execution of the function will start from the beginning

;start again the function:

push ecx                      ; ecx has a value 1

mov eax, [esp+1 ]       ; eax gets 0 – the value of the parameter

cmp eax, 0                  ; now it’s equal, so no jump

ja els                           ; no jump

mov eax, 0

jmp dun

……

dun:     pop ecx                      ; ecx will have value 1, the esp will return

; to the return  address

ret                               ; function will return to the line add esp, 4 and

; esp will return to the address of the value of parameter

……

; after we came back from the function call

add esp, 4                 ; will return esp to the position that was before function call

; parameter 0 will be taken out of stack

add eax, ecx             ; eax = eax +ecx= 0 + 1

dun:   pop ecx                     ; ecx gets ** ** ** ** , esp returns to the position

; of the return address in

; C++ code

ret                            ;  will return us to the main function in C++ with value 1 in eax

; esp will return to the position of the parameter that

; was pushed inside the stack

; before function call

after the program will return to main the following command will be performed in the “background”:

add esp, 4 – it will return the value of the stack to the initial position

Functions with two and more parameters

Code in C++

#include <iostream>

using namespace std;

// function prototypes

extern “C” int sum ( int a, int b);

extern “C” int abs ( int a);

extern “C” int power ( int base,  int exponent);

int main(){

int a, b, base, exponent;

cout << “ enter 4 integers \n”;

cin >> a>> b>> base >> exponent;

int c = sum ( a, b);

int powRes = power ( base, exponent);

cout << c < powRes;

return 0;

}

Assembly code for functions sum , abs and power:

global sum

sum: push ebx

push ecx

mov ebx, [esp + 16]

mov ecx , [esp + 12]

add ebx, ecx

move eax, ebx

pop ebx

pop ecx

ret

global abs

abs:      push ebx

mov ebx, [esp +4]

cmp ebx, 0

jae end

neg ebx

end:     mov eax, ebx

pop ebx

ret

global power

power: push ebx

push ecx

mov ebx, [esp+12]

mov ecx, [esp +16]

mov eax, 1

cmp ecx, 0

ja rpt

jmp dun

rpt:       mul ebx

dec ecx

jnz rpt

dun:       pop ecx

pop ebx

ret